## Slide 1: Asynchronous Deterministic Networking (ADN) Framework for Large scale networks
draft-joung-detnet-asynch-detnet-framework-02
Jinoo Joung, Jeong-dong Ryoo, Tae-sik Cheung, Yizhou Li, Peng Liu
Design Team meeting, April 12

## Slide 2: Overview of the Draft
Framework for Latency Guarantee
  Regulation based
    Asynchronous Traffic Shaping (ATS)
    Flow Aggregate Interleaved Regulators (FAIR)
    Port-based Flow Aggregate Regulators (PFAR)
  Packet meta-data based
    Work-conserving stateless core fair queuing (C-SCORE)
Framework for Jitter Guarantee
  Buffered network
Today’s focus is on the operational procedures

## Slide 3: Work Conserving Stateless Core Fair queuing (C-SCORE)
Framework
  FT, Finish time F(p) = Service order of packet p. Smaller FT gets earlier service.
  At entrance node 0: F0(p) = max{F0(p-1), A0(p)} + L(p)/r;
  At core node h: Fh(p) = Fh-1(p) + dh(p).
If dh(p) = Lmaxh-1/Rh-1 + L/r,
Then the E2E latency of p’s flow is bounded [Kaur] by
B, L, r are flow specific, which can be controlled according to requirement  Latency bound can be adjusted if necessary
Symbol | Definition
Fh(p) | ‘Finish time’ of packet p at node h
Ah(p) | Arrival time of p at h
L(p) | Length of p
L | Max Packet Length of p’s flow
r | Service rate of p’s flow
B | Max Burst size of p’s flow
Lmaxh | Max Packet Length at node h
Rh | Link capacity of h
H | Last node of p’s path
PGPS | Packetized Generalized Processor Sharing
is the only term external & can be negligible.
This bound is same with a stateful fair queuing network (PGPS, etc.)

## Slide 4: C-SCORE: Operational procedures
Network configuration stage
  A source requests latency bound for flow i, with specifying its and Bi
  If the latency bound can be met, admit the flow
  Network reserves the links in the path such that
    and , for all h
The entrance node or the source
  Maintains the flow state, i.e. F0(p-1) & r.
  Maintains a clock, for A0(p).
  Maintains the link info Lmax0/R0.
  Upon receiving or generating packet p,
    Obtains F0(p) = max{F0(p-1), A0(p)} + L(p)/r. Use it as the FT in 0. Put p in a sorted queue.
    Obtains F1(p) = F0(p) + Lmaxh-1/Rh-1 + L/r.
    Records F1(p) & L/r in the packet as meta-data for the use in the next node 1.
  Update the flow state to F0(p).
A core node h
  Maintains the link info Lmaxh/Rh. (A rather static value)
  Upon receiving packet p,
    retrieve meta-data Fh(p) & L/r, use Fh(p) as the FT. Put p in a sorted queue.
    Obtain Fh+1(p) = Fh(p) + Lmaxh/Rh + L/r.
    Update Fh(p) with Fh+1(p) before or during p is in the queue.
Symbol | Definition
Fh(p) | ‘Finish time’ of packet p at node h
A0(p) | Arrival time of p at node 0
L(p) | Length of p
L | Max Packet Length of p’s flow
 | Arrival rate of flow j
Bj | Max burst of flow j
r | Service rate of p’s flow
 | Service rate of flow j at node h
Lmaxh | Max Packet Length at node h
Rh | Link capacity of h
f(h) | Set of flows in node h
Symbol | Definition
Fh(p) | ‘Finish time’ of packet p at node h
A0(p) | Arrival time of p at node 0
L(p) | Length of p
L | Max Packet Length of p’s flow
 | Arrival rate of flow j
Bj | Max burst of flow j
r | Service rate of p’s flow
 | Service rate of flow j at node h
Lmaxh | Max Packet Length at node h
Rh | Link capacity of h
f(h) | Set of flows in node h

## Slide 5: C-SCORE with FIFO: Operational procedures
Network configuration stage
  A source request latency bound, with specifying its and Bj
  If the latency bound can be met, admit the flow
  Network reserves the links in the path such that
    and , for all h
The entrance node or the source
  Maintains flow state, i.e. F0(p-1) & r.
  Maintains a clock (for A( )).
  Maintains the link info Lmax0/R0.
  Upon receiving packet p,
    Obtains F0(p) = max{F0(p-1), A0(p)} + L(p)/r. Use it as the FT in 0. Put p in a sorted queue.
    Obtains F1(p) = F0(p) + Lmaxh-1/Rh-1 + L/r.
    Records F1(p), L, r in the packet as meta-data for the use in the next node 1.
  Update the flow state to F0(p).
A core node h
  Maintains the link info Lmaxh/Rh. (A rather static value)
  Upon receiving packet p,
    retrieve Fh(p), L, r, use Fh(p) as the FT.
    Using L & r, put p in the FIFO queue assigned for the flows of the same or similar type.
    Obtain Fh+1(p) = Fh(p) + Lmaxh/Rh + L/r.
    Update Fh(p) with Fh+1(p) before or during p is in the queue.
Input
port
S
Node =
output port module
output port module
Input
port
Switching device
High
priority
Low
priority
Low priority queue
Strict priority
Scheduler with pre-emption
FIFO queue for similar flows
FIFO queue for similar flows
M
M: Meta-data retrieve & update; FIFO enqueue
S: HoQ examine, Select the packet with min FT
Core node with FIFO
Red letters: the only differences from the previous page

## Slide 6: C-SCORE Summary
C-SCORE with dh(p) = Lmaxh-1/Rh-1 + L/r
  Has a theoretical E2E latency bound,
  Needs a clock at the source or entrance node,
  Needs a sorted queue,
  Needs a meta-data of Fh(p), L/r
  Needs to update meta-data, but not upon the packet’s transmission.
C-SCORE with dh(p) = Lmaxh-1/Rh-1 + L/r with FIFO per flow type (of the same L and r)
  Shows similar performance
  Needs similar things, but needs the meta-data Fh(p), L, r
  Does not need a sorted queue
They both perform as if the stateful fair queuing schedulers are placed in all the nodes, which are known as the best statistical-multiplexing schedulers.

## Slide 7: Jitter guarantee framework: BN [BN, ADN]
Basic idea: Jitter guarantee ≈ Reproducing the inter-arrival process with the inter-departure process of a network.
With a latency guaranteed network, time-stamping, and buffering at the network boundary; Hold packets as follows:
Properties
  E2E jitter is upper bounded, by (U+g-m)+.
  ‘E2E buffered latency’ (ci – ai) is also upper bounded by (U-W+m).
  We can control the jitter bound by selecting m.
  We can have zero jitter by setting m=U+g, with E2E buffered latency bound (2U+g-W) ≈ 2U.
Source
Network with E2E latency upper bound guarantee
Destination
Buffer
an
bn
cn
Time-stamper

## Slide 8: Buffered Network Operations
The time-stamper, TS (at the source or entrance node),
  maintains a clock (that does not need to be synched with other nodes)
  time-stamps a packet upon
    its generation (if TS is in the source) or
    its arrival (if TS is in the entrance node)
Network does nothing (just guarantees latency)
The buffer (at the destination or the last node)
  holds the packet according to the rule & releases
Note: Time-stamping:
  is similar to the 1-step PTP
  but not upon a packet’s transmission
  Stamped Time can be placed in the RTP timestamp field or the packet header as meta-data. It is A0(p) in the C-SCORE, which was anyway maintained by the source or entrance node.
Source
Network with E2E latency upper bound guarantee
Destination
Buffer
an
bn
cn
Time-stamper

## Slide 9: Thank you
Please take a look at
  https://datatracker.ietf.org/doc/draft-joung-detnet-asynch-detnet-framework/
Comments and Questions are welcome!
[Kaur] Jasleen Kaur, and Harrick M. Vin. "Core-stateless guaranteed rate scheduling algorithms." In Proceedings IEEE INFOCOM 2001. Conference on Computer Communications. Twentieth Annual Joint Conference of the IEEE Computer and Communications Society (Cat. No. 01CH37213), vol. 3, pp. 1484-1492. IEEE, 2001.
[FAIR] Jinoo Joung. "Framework for delay guarantee in multi-domain networks based on interleaved regulators." Electronics 9, no. 3 (2020).
[ADN] Jinoo Joung, Juhyeok Kwon, Jeong-Dong Ryoo, and Taesik Cheung. "Asynchronous Deterministic Network Based on the DiffServ Architecture." IEEE Access 10 (2022).
[Zhang] Lixia Zhang. "Virtual clock: A new traffic control algorithm for packet switching networks." In Proceedings of the ACM symposium on Communications architectures & protocols, pp. 19-29. 1990.
[Stoica] Ion Stoica and Hui Zhang. "Providing guaranteed services without per flow management." ACM SIGCOMM Computer Communication Review 29, no. 4 (1999): 81-94.
[Stiliadis] Dimitrios Stiliadis and Varma Anujan. "Rate-proportional servers: A design methodology for fair queueing algorithms." IEEE/ACM Transactions on networking 6, no. 2 (1998): 164-174.
[BN] Jinoo Joung and Juhyeok Kwon. "Zero jitter for deterministic networks without time-synchronization." IEEE Access 9 (2021).