## Slide 1
IETF work for TM-RID
Work items in IETF
Related to TM-RID
Mostly with HIP
Robert Moskowitz
July 22, 2019

## Slide 2
Hierarchical HITs
Old draft exists for HHITs
  draft-moskowitz-hierarchical-hip-06.txt
Provides for distributed registries HITs
  The devil is in the details (sec 4.1)
    Two levels of hierarchy? How many bits?
Crypto agility
  Only ECDSA/hier/SHA-256 defined in draft
  How to manage more and future algorithms

## Slide 3
HHITs Registries
Registry services
  Separate into own draft?
  Who registers registries?
Proof of registration
  Lookup at Registry
  Certificates for client HHITs
    Add Concise Identities
      Draft-birkholz-core-coid
  ‘Raw’ signatures

## Slide 4
HHITs Registries
Additional services
  Extract from
    draft-moskowitz-hip-based-5gpp-ip-mobility
  RVS services
    Federation of RVS
    Forwarding I1 from ‘own’ RVS to ‘foreign’ RVS?

## Slide 5
Other HIP work
Crypto, crypto and more crypto
  How to manage and bound growth of YAA
  Yet stay current with NIST and other
New, lightweight crypto
  Still ‘under development’ per NIST
More?

## Slide 6
Concise Binary Object Representation CBOR
Use CWT (CBOR tokens) throughout
  Including new HIP payload formats? Is there value here?
    Register HIP parameters with CBOR?
Concise Identities alternative to X.509
  draft-birkholz-core-coid
  Death to ASN.1! :)
More?

## Slide 7
OAUTH
OAUTH has been included in ASTM work
Add HIP as OAUTH method
  What does this entail?
  Who will do it?

## Slide 8
RemoteID Message Format
Only up to 24 bytes of data space to work with
  Fit in Bluetooth advertisement data field for single beacon message
5 primary types
  Basic ID, Authentication, Self ID, Location, & Operator
  Basic ID & Location required
Spec document can be found: https://github.com/opendroneid/specs

## Slide 9
Proposed Auth Message Format
For OpenID type HIT
Format to carry hashes of previous messages sent and a signature on hash list
Provide provenance of sent messages in given time period
16 pages of data available to use

## Slide 10
Loose ends
There is always something left out
What is it?